IEEE TRANSACTIONS ON MEDICAL IMAGING, VOL. 18, NO. 10, OCTOBER 1999

Elastic Model-Based Segmentation of 3-D Neuroradiological Data Sets

Andr´abor Sz´

as Kelemen, G´ekely,* and Guido Gerig

Abstract— This paper presents a new technique for the automatic model-based segmentation of three-dimensional (3-D) objects from volumetric image data. The development closely follows the seminal work of Taylor and Cootes on active shape models, but is based on a hierarchical parametric object description rather than a point distribution model. The segmentation system includes both the building of statistical models and the automatic segmentation of new image data sets via a restricted elastic deformation of shape models. Geometric models are derived from a sample set of image data which have been segmented by experts. The surfaces of these binary objects are converted into parametric surface representations, which are normalized to get an invariant object-centered coordinate system. Surface representations are expanded into series of spherical harmonics which provide parametric descriptions of object shapes. It is shown that invariant object surface parametrization provides a good approximation to automatically determine object homology in terms of sets of corresponding sets of surface points. Gray-level information near object boundaries is represented by 1-D intensity proﬁles normal to the surface. Considering automatic segmentation of brain structures as our driving application, our choice of coordinates for object alignment was the well-accepted stereotactic coordinate system. Major variation of object shapes around the mean shape, also referred to as shape eigenmodes, are calculated in shape parameter space rather than the feature space of point coordinates. Segmentation makes use of the object shape statistics by restricting possible elastic deformations into the range of the training shapes. The mean shapes are initialized in a new data set by specifying the landmarks of the stereotactic coordinate system. The model elastically deforms, driven by the displacement forces across the object’s surface, which are generated by matching local intensity proﬁles. Elastical deformations are limited by setting bounds for the maximum variations in eigenmode space. The technique has been applied to automatically segment left and right hippocampus, thalamus, putamen, and globus pallidus from volumetric magnetic resonance scans taken from schizophrenia studies. The results have been validated by comparison of automatic segmentation with the results obtained by interactive expert segmentation.

Index Terms— Automatic 3-D segmentation, elastically deformable surface models, statistical shape models.

Manuscript received March 1, 1999; revised June 18, 1999. The Associate Editors responsible for coordinating the review of this paper and recommending its publication were M. Viergever and W. Niessen. Asterisk indicates corresponding author.

A. Kelemen and *G. Sz´ekely are with the Computer Vision Laboratory, Swiss Federal Institute of Technology, ETH-Zentrum, CH-8092 Zurich, Switzerland (e-mail: szekely@vision.ee.ethz.ch).

G. Gerig is with the Department of Computer Science and Psychiatry, University of North Carolina, Chapel Hill, NC 27599-3175 USA and with the Department of Psychiatry, University of North Carolina, Chapel Hill, NC 27599-3175 USA.

Publisher Item Identiﬁer S 0278-0062(99)09109-0.

I. INTRODUCTION EGMENTATION of anatomical objects from large three-dimensional (3-D) medical data sets, obtained from routine magnetic resonance imaging (MRI) examinations, for example, represents a necessary yet difﬁcult issue in medical image analysis. With the steady increase of routine use of 3-D imaging methods such as MRI, computer tomography (CT), and 3-D ultrasound in radiological diagnosis, monitoring, radiotherapy, and surgical planning, for example, there is a clear need for improved and efﬁcient methods for the extraction of anatomical structures and for a description by morphometric analysis. In some limited applications, segmentation can be achieved with minimal user interaction by applying simple and efﬁcient image processing methods, which can be applied routinely [8]. In many clinical applications, such as computer assisted neurosurgery or radiotherapy planning, a large number of organs must be identiﬁed in the radiological data sets. While a careful and time-consuming analysis may be acceptable for outlining complex pathological objects, no real justiﬁcation for such a procedure can be found for the delineation of normal healthy organs at risk. Delineation of organ boundaries is also necessary in various types of clinical studies, where the correlation between morphological changes and therapeutical actions or clinical diagnosis must be analyzed. In order to get statistically signiﬁcant results, a large number of data sets must be segmented. For such applications manual segmentation becomes questionable, not only because of the amount of work, but also with regard to the poor reproducibility of the results. The necessity of obtaining high reproducibility and the need to increase efﬁciency motivates the development of computer-assisted automated procedures.

II. MODEL-BASED SEGMENTATION
OF 3-D RADIOLOGICAL DATA

Elastically deformable contour and surface models, so-called snakes [9], have been proposed as tools for supporting manual object delineation. While such procedures can be extended to 3-D [4], [29], their initialization is a critical issue. Most often, the initial guess must be very close to the sought contour to guarantee a satisfying result [16]. An excellent overview of elastically deformable models can be found in [13]. The primary reason for the need of a precise snake initialization is the presence of disturbing attractors in the image. These attractors do not belong to the object contour,

0278–0062/99$10.00 © 1999 IEEE